Instructions for px4fmu-v3_6_12_2017

1. Plug in the pixhawk to the computer through the USB and start QgroundControl. Once it is started click on the gear symbol (settings) and then the firmware button. You will want to load a custom version onto the pixhawk. Navigate to the directory and select the px4fmu-v3_default.px4 file.
2. Basically you will now go down the side bar of buttons and set up the Osprey. Under “Airframe” there will be “Helicopter” and a pull down menu. In the pull down menu will be the “Rotormast Osprey V22”. Select it and then hit the “Apply and Restart” button.
3. Radio. You will do the calibration. Just follow the directions and do what it says. One trick I’ve started doing is right before you set for/aft limits, make sure you center the collective and the nacelle. This will get the trim position set right. Also make sure the throttle and pitch curves are linear and at +/-100%. Set the flap channel to the collective channel. Mine was channel 6. The “Aux 1 RC Passthrough” channel is set to the nacelle channel. Mine was channel 12.
4. Sensors. Just go down the list and follow the directions. I placed the pixhawk on the left side under the wing with the arrow pointing forward which leaves the servo leads at the back. This corresponds to a “Rotation Roll 270”
5. Flight modes. This sets up the RC switches to change to different modes. I used channel 17 on mine which is a digital channel on my 18MZ. You want the switch to be in manual or aero mode so set it up on whatever channel and switch you wish to use.
6. Power. Use the calculator button and a volt meter to set up the battery display to be more accurate. It is also used to determine when to automatically land so it needs to be fairly accurate. DO NOT use the calibrate ESC. We are not a multirotor...
7. Parameters. This is the area that can set a whole bunch of stuff. Use the scroll wheel on the mouse to move up/down the buttons and the text area. I changed the following from default.
  - PWM Outputs
    - PWM_DISARMED 1000us
    - PWM_RATE 50Hz
  - Radio Calibration
    - Just make sure things look like they are set correctly like number of channels, channel selection, trim values, etc.

Setup of servos

This is where we have to mess with a file on the SD card in the pixhawk. This is the tedious part. The file consists of several lines of input. Note that all numbers in the file are integers even though they represent floating point values. Each is divided by 10000 internally to the program. Therefore 10000 / 10000 = 1.0 and 4000 / 10000 = 0.4 My file is shown below…

A: 0 5000 5000 2500 2500 4000 4000
P: -7000 -3500 0 4500 10000
Q: -10000 -5000 -2500 0 7000
X: 0 -10000 1000 10000
X: 1 -10000 1000 10000
X: 2 -10000 0 10000
X: 3 -10000 0 10000
X: 4 -10000 -200 10000
X: 5 -10000 -1000 10000
X: 6 -10000 0 10000
X: 7 -10000 0 9500

A: defines setup mode and the overall volume that each primary control can use.
1. The first number is a boolean for setup mode. Setting this to 1 will pass the primary controls directly into the mixer. Use this for initial setup of the vehicle. Setting it to 0 will be how it normally runs and will let the gyros affect the outputs.
2. Left nacelle for/aft volume
3. Right nacelle for/aft volume
4. Left nacelle roll volume
5. Right nacelle roll volume
6. Left nacelle collective volume
7. Right nacelle collective volume

P: and Q: are the same. P: is for the left nacelle and Q: is for the right and it is a 5 point collective curve. Just play around with the numbers to get both nacelles to match pitch values. You will want it to go from -6 to 18 with setup mode on.

X: defines the min/max and center values for each of the output servos. Use this to set the center offsets and limits as needed. If you need to reverse a servo, just swap the min/max values. Normally the values are -10000 0 10000 would now become 10000 0 -10000.
1. Id number of servo
2. min value
3. center value
4. max value